## Slide 1: Optimal Train Routing and Scheduling
Case Study – Final Presentation
Fabian Bleile, Sándor Daróczi, Simon Ramoser, Tobias Müller

## Slide 2
No, not again!
https://www.openpetition.de/petition/online/umsteigen-im-muenchner-hauptbahnhof-leichter-machen-bau-einer-zusaetzlichen-bahnsteigverbindung
https://www.derwesten.de/panorama/vermischtes/deutsche-bahn-zug-verspaetung-app-entschaedigung-ausfall-id233567353.html

## Slide 3: Agenda
01
Problem Description
02
Combined Approach
03
Decoupled Approach
04
Experiments
05
Summary

## Slide 4: Problem Description
A
B
C
D
Train 1
Train 2
Train 3

## Slide 5: Problem Description
A
B
C
D
Train 1
Train 2
Train 3
What should Trains 2 and 3 do to minimize overall delay?

## Slide 6: Problem Description
A
B
C
D
Train 4
Whole network might be affected
Exponentially many routes in general
It can be shown that the problem is NP-hard
Conflict
Train 3
Train 2
Train 1

## Slide 7: Problem Description
Additionally, train dynamics also have to be considered:
  Acceleration
  Braking
  Maximum speed
  …

## Slide 8: Problem Description
Optimization Problem
Inputs
1
Goal
2
Objective
3

## Slide 9: Problem Description
Railway network with initial schedules and delays
weight
Parameters for train dynamics
A
B
C
D
Inputs
1

## Slide 10: Problem Description
Optimization Problem
Inputs
1
Goal
2
Objective
3
weight
A
B
C
D

## Slide 11: Problem Description
Compute a set of feasible routes and schedules
2. Determine speed profiles
A
B
C
D
Goal
2

## Slide 12: Problem Description
Optimization Problem
Inputs
1
Goal
2
Objective
3
weight
A
B
C
D
A
B
C
D

## Slide 13: Problem Description
: total delay of train
: energy consumption of train
Objective
3

## Slide 14: Problem Description
Optimization Problem
Inputs
1
Goal
2
Objective
3
weight
A
B
C
D
A
B
C
D

## Slide 15: Desired Output

## Slide 16: Agenda
01
Problem Description
02
Combined Approach
03
Decoupled Approach
04
Experiments
05
Summary

## Slide 17
Dynamics: One Train, One Segment
segment

## Slide 18
T
Dynamics: One Train, One Segment
segment

## Slide 19
Optimal Control Problem
such that
+ boundary conditions

## Slide 20
Preprocessing
1
Modeling
2
Solving
3
How to Merge the Segment Dynamics?

## Slide 21: Preprocessing
Compute set of routes for each train
Preprocessing
1
Modeling
2
Solving
3
A
B
C
D

## Slide 22: Optimization Model
For each train t : variables ,
Preprocessing
1
Modeling
2
Solving
3
C
D
A
B

## Slide 23: Optimization Model
Preprocessing
1
Modeling
2
Solving
3
B
A

## Slide 24: Conflict Constraints
Preprocessing
1
Modeling
2
Solving
3
C
D
A
B

## Slide 25: Conflict Constraints
Green first
Orange first
Preprocessing
1
Modeling
2
Solving
3
Order of trains:

## Slide 26: Optimization Model Overview
Train rides
Framework
Mixed Integer Optimal Control Problem
Preprocessing
1
Modeling
2
Solving
3
…
…
…
A
B
C
D

## Slide 27: Solving the Problem
Preprocessing
1
Modeling
2
Solving
3
Mixed Integer Optimal Control Problem
Mixed Integer Nonlinear Program
Direct multiple shooting
(with forward Euler)

## Slide 28: Agenda
01
Problem Description
02
Combined Approach
03
Decoupled Approach
04
Experiments
05
Summary

## Slide 29: Combined vs. Decoupled Approach
Combined
Decoupled

## Slide 30: Combined vs. Decoupled Approach
Mixed Integer Optimal Control Program (MIOCP)
Solution
Combined
Decoupled
Network, Schedule
Trains

## Slide 31: Combined vs. Decoupled Approach
Combined Approach
Combined
Decoupled
Route-based ansatz (simplified dynamics)
Segment-based ansatz (no dynamics)
Mixed Integer LP
One route per train
Train order
Network, Schedule
Trains
Solution

## Slide 32: Route-based Ansatz
Preprocessing routes
Conflict constraints
Speed:
  Time difference as notion of speed
  Bound max average speed:
Dynamics
What changes
What to keep

## Slide 33: Linearized Dynamics
Bound speed change  Bound time difference change
Goal: Express in linear constraints
Example: Start with and accelerate with

## Slide 34: Time difference bounds: Example
T2 – T1 = 100s; T3 – T2 = 55s  f(100) ≥ 55
T3 – T2 = 55s; T4 – T3 = 45s  f(55) ≥ 45
…
Speed
Time t
100s
55s
45s
37s

## Slide 35: Time difference bounds
(40 s, 50 s)
g
(100 s, 55 s)
(55 s, 45 s)
Notes: v_max = 70, granularity = 1000, acc_max = 0.1

## Slide 36: Linearized Dynamics: PWL Approximation
Feasible speed changes
(100 s, 80 s)
Notes: v_max = 70, granularity = 1000, acc_max = 0.1

## Slide 37: Linearized Dynamics: Example
distance in m
velocity in m/s
Green train: output of MILP with dynamics modeled with linear constraints
Red train: output of combined approach
Notes: v_max = 70, granularity = 4000, acc_max = 0.1

## Slide 38: Segment-based Ansatz
Segment-based ansatz (no dynamics)
Mixed Integer LP
One route per train
Train order
Combined Approach
Route-based ansatz (simplified dynamics)
Network, Schedule
Trains
Solution

## Slide 39: Segment-based Ansatz
Conflict constraints
What changes
What to keep
No dynamics
Segment variables
Speed bounds
Notes: Say: „Routes will be determined by segment variables“

## Slide 40: Model Complexity
Combined
Decoupled route-based
Nonlinear Constraints
Binary
Variables
Decoupled segment-based
# trains
# segments
Notes: Theoretically, that‘s nice, but let‘s see how this looks in practice!

## Slide 41: Agenda
01
Problem Description
02
Combined Approach
03
Decoupled Approach
04
Experiments
05
Summary

## Slide 42: Choice of

## Slide 43: Test Examples
Intro Example
17 Segments
4 Trains
CAIMI (Literature)
23 Segments
4 Trains
Y-Network
3 Segments
2 Trains

## Slide 44: Total Objective

## Slide 45: Decoupled Route-based vs. Segment-based
40 Segments
5 Trains
Green trains: output route-based
Red trains: output segment-based
Notes: Motivation: in reality multiple complex parts (stations) are connected via few (long) segments

## Slide 46: Decoupled Route-based vs. Segment-based

## Slide 47: Agenda
01
Problem Description
02
Combined Approach
03
Decoupled Approach
04
Experiments
05
Summary

## Slide 48: Summary
B
Problem
Input
Output
Objective
A
B
weight
A
B

## Slide 49: Summary
B
Problem
Input
Output
Objective
Approach

## Slide 50: Summary
B
Approach
Decoupled
Combined

## Slide 51: Summary
B
Problem
Input
Output
Objective
Approach
Decoupled
Combined
Conclusion
Combined:
More accurate
Decoupled:
More efficient

## Slide 52
Notes: This example has:
159 segments
134 connectors
20 stations
9 trains
Interesting fact about runtime:
~4min for dynamic part
~12min for discrete part
 now, the discrete part is the computational bottleneck

## Slide 53: Backup-Slides

## Slide 54
Egal wie gut du fährst, Züge fahren Güter.
~ Jan Delay

## Slide 55: Outlook
What have we done additionally?
Greedy algorithm by Fabi
Heuristic Conflict Based Search (CBS)
Model dynamics as path through speed graph (nodes = different speeds and edge if train can reach next speed in next segment)
Refine pwl dynamics by simplifying dynamics around stations
…
What could have been done?
Segment-based combined approach
Job-shop scheduling for solving the discrete part (segments = machines, trains = jobs)
Multi-commodity flow for solving discrete part
Separation Oracle for route-based discrete parts (?)
Choose only ‚good‘ routes from the exponential-sized set of routes
Merge decoupled approaches to solve huge networks
Solve local areas and combine to solve huge networks
Reduce conflict constraints when conflict is unlikely (relevant for route-based approach)

## Slide 56: Assumptions for simplification
• Trains have no length • A train arrives at a station once it reaches the exact center of the corresponding segment • We do not respect complex physical laws, so only basic physics are assumed

## Slide 57: Hardness

## Slide 58: Moving Trains in decoupled approach
Decoupled approach
The simpler the dynamics in MILP - the higher the approximation error
Approximation error 2 trains, one switch
(MILP) Compute routes and track occupancy using
simplified dynamics
(OCP) Compute optimal trajectories

## Slide 59: Approximation Error Example
Red train
max speed 40 m/s
lightweight
Blue train
max speed same as red
heavyweight
Minimize sum of delays here
Optimal: Red before Blue Train
Which train enters the common segment first?

## Slide 60: Spectrum of 'simplified dynamics'
No dynamics: arbitrary speed changes from segment to segment
PWL-approximated dynamics: controlled speed changes on subsegments

## Slide 61: Segment-based Ansatz
Binary decision variables
Routes (sequence of segments) for each train ()
Train order on segments for each pair of trains ()
…
Continuous decision variables
Segment occupation intervals
…
Segment occupation for segment s

## Slide 62: Total Delay

## Slide 63: Runtime
Notes: Questions
Which models are most complex (number of binary variables, non-linear constraints, …)
Is the complexity reflected in the runtime of the corresponding pipelines?
Assumption: w.l.o.g. trains cannot go over segments twice
Note: for the decoupled route-based approach, there are two bottlenecks in terms of runtime:
the preprocessing to find routes (enumerating all routes is exponential in general (in K_n, there are ⌊(n−2)!e⌋ paths between each pair of vertices), k-shortest paths is pseudo-polynomial (O(kn(m+nlogn))))
the dynamic part with its nonlinear constraints
Possible recommendation: since realistic networks are often only complex locally near stations and trains are slow there, neglect dynamics inside stations
Use combined approach globally on a simplified network (where all stations are simplified to parallel segments between the same two connectors)
Use segment-based discrete part locally in complex parts of the network to route the trains there (as it is done e.g. in the Dang paper)

## Slide 65
Notes: Optimal solution in 2s :’D

## Slide 66
Combined Approach
Network, Schedule
Trains
Solution
Route-based ansatz (simplified dynamics)
[Section 4.2]
Segment-based ansatz (no dynamics)
[Section 4.3]
Mixed Integer LP
[Section 4.4]
Mixed Integer Optimal Control Program (MIOCP)
Solution
Network, Schedule
Trains

## Slide 68: References
[1] Joel A E Andersson, Joris Gillis, Greg Horn, James B Rawlings and Moritz Diehl. ‘CasADi – A software framework for nonlinear optimization and optimal control’. In: Mathematical Programming Computation (2018).
[2] Jerome Berclaz, Engin Turetken, Francois Fleuret and Pascal Fua. ‘Multiple Object Tracking using K-Shortest Paths Optimization’. In: IEEE Transactions on Pattern Analysis and Machine Intelligence 33 (2011), pp. 1806–1819. doi: https://doi.org/10.1109/TPAMI.2011.21. url: http://infoscience.epfl.ch/record/164041.
[3] Gabrio Caimi, Fabian Chudak, Martin Fuchsberger, Marco Laumanns and Rico Zenklusen. ‘A new resource-constrained multicommodity flow model for conflict-free train routing and scheduling’. In: Transportation science 45.2 (2011), pp. 212–227.
[4] Andrea D’Ariano, Marco Pranzo and Ingo A. Hansen. ‘Conflict Resolution and Train Speed Coordination for Solving Real-Time Timetable Perturbations’. In: IEEE Transactions on Intelligent Transportation Systems 8.2 (2007), pp. 208–222. doi: 10.1109/TITS.2006.888605.
[5] Quoc Khanh Dang, Thomas Bourdeaud’Huy, Khaled Mesghouni and Armand Toguyeni. ‘Low-Level Modeling for Optimal Train Routing and Scheduling in Busy Railway Stations’. In: International Journal of Transport and Vehicle Engineering (2019). url: https://hal. science/hal-03462793.
[6] J. Du and J.Y.-T. Leung. ‘Minimizing total tardiness on one machine is NP-hard’. In: Math. Oper. Res. 15.3 (1990), pp. 483–495.
[7] Omid Gholami, Yuri Sotskov and Frank Werner. ‘Job-Shop Scheduling with Objectives Appropriate for Train Scheduling in a Single-Track Railway’. In: July 2012.
[8] Banafsheh Khosravi, Julia Bennell and Chris Potts. ‘Train scheduling and rescheduling in the UK with a modified shifting bottleneck procedure’. In: OpenAccess Series in Informatics 25 (Jan. 2012), pp. 120–131. doi: 10.4230/OASIcs.ATMOS.2012.120.
[9] Paola Pellegrini, Gr ́egory Marli`ere and Joaquin Rodriguez. ‘Optimal train routing and scheduling for managing traffic perturbations in complex junctions’. In: Transportation Research Part B: Methodological 59 (2014), pp. 58–80.
[10] Ben Roberts and Dirk P. Kroese. ‘Estimating the Number of s-t Paths in a Graph’. In: Journal of Graph Algorithms and Applications 11.1 (2007), pp. 195–214. doi: 10.7155/jgaa.00142.
[11] Mauricio Salerno, Yolanda E-Mart ́ın, Raquel Fuentetaja, Alba Gragera, Alberto Pozanco and Daniel Borrajo. ‘Train Route Planning as a Multi-agent Path Finding Problem’. In: Advances in Artificial Intelligence. Ed. by Enrique Alba, Gabriel Luque, Francisco Chicano, Carlos Cotta, David Camacho, Manuel Ojeda-Aciego, Susana Montes, Alicia Troncoso, Jos ́e Riquelme and Rodrigo Gil-Merino. Cham: Springer International Publishing, 2021, pp. 237–246.
[12] Marcella Sam`a, Paola Pellegrini, Andrea D’Ariano, Joaquin Rodriguez and Dario Pacciarelli. ‘Ant colony optimization for the real-time train routing selection problem’. In: Transportation Research Part B: Methodological 85 (2016), pp. 89–108.
[13] Yihui Wang, Bart De Schutter, Ton JJ van den Boom and Bin Ning. ‘Optimal trajectory planning for trains–a pseudospectral method and a mixed integer linear programming approach’. In: Transportation Research Part C: Emerging Technologies 29 (2013), pp. 97–114.